## Slide 1: Build Real-Time Controller Code (Exercise-2)

## Slide 2
DETAILED INSTRUCTIONS:
Description of Exercise 2:
This project contains the System on Module (sbRIO-9651) and CLIP required for this exercise.
To expand the hierarchy and reveal the content of the project, click the “+” boxes next to each part of the sbRIO system and measurement modules listed.
Explore the LabVIEW Project
Explore the project and expand the hierarchy on the project
FPGA Code
FPGA Target
RT Target
Host Computer

## Slide 3
DETAILED INSTRUCTIONS:
Open the VI Package Manager
Navigate to Tools >> VI Package Manager to open the VI Package Manager
Search for “cRIO”
To install the cRIO Waveform Library, search for “crio”.
Find NI Compact RIO Waveform Library in the list.
We will use this library for rest of our exercise as it has both FPGA and RT code templates which will reduce code development for Acquisition Projects on the Real-Time OS.
Install cRIO Waveform Library (Required Component)

## Slide 4
DETAILED INSTRUCTIONS:
Open the Installer
Double Click on the “NI CompactRIO Waveform Library” in VI Package Manager to start the installion
Install the Package
Click on the install button to start the installation of the waveform library
Accept the License Agreement to continue the installation
Click “Finish” to finish the installation
<Double Click>
Install cRIO Waveform Library (..Contd)

## Slide 5
DETAILED INSTRUCTIONS:
Open Ex-2 FPGA.vi
  Double-click on the file named Ex-2 FPGA.vi located under the FPGA target in the project
Open the Block Diagram The block diagram contains a While Loop with a sequence structure embedded to enforce loop timing. The cRIO waveform FPGA template contains three sequences:
Initialization State
Interrupt to inform start of FPGA to Real-Time OS
Acquisition Loop
We will modify this FPGA VI to acquire input from a microphone using the content from the previous exercise.
A. Initialization
B. Interrupt to Real-Time OS
C. Acquisition Loop
Open the Ex-2 FPGA.vi and look at its block diagram
The Ex-2 FPGA.vi is located under the FPGA target in the hierarchy. This VI already contains timing code to use for this exercise.
DMA FIFO to Transfer Data to
Host
Timer to control
Acquisition timing
Placeholder for Analog Input

## Slide 6
DETAILED INSTRUCTIONS:
Open the Ex-1 FPGA Soln.vi
  Double-click on the file named Ex-1 FPGA.vi which is located under the FPGA target in the hierarchy as shown in Figure A
Select Highlighted Code
Select the code highlighted with red box in the picture to create subVI. To create subVI from the selected section, navigate to Edit >> Create subVI after the selecting the highlighted code
Create “SPI Engine Microphone ADC” subVI
Group SPI Engine on FPGA into subVI

## Slide 7
DETAILED INSTRUCTIONS:
Save the subVI as SPI Engine Microphone ADC
Change the Front Panel Connector Interface
Modify the interface by assigning the appropriate controls on the front panel.
Modify the Icon of the subVI
Change the icon name to “SPI CMDS MIC” as shown in the picture
Modify “SPI Engine Microphone ADC.vi” subVI Front Panel
Modify the Front Panel interface of “SPI Engine Microphone ADC.vi”
Enable Lines
DIO Lines
SPI References

## Slide 8
DETAILED INSTRUCTIONS:
Open the Ex-1 FPGA.vi
  Double-click on the file named Ex-1 FPGA.vi is located under the FPGA target in the hierarchy
Open the Block Diagram
  Select the code highlighted with red box in the picture to create subVI. To create subVI from the selected section, navigate to Edit >> Create subVI after the selecting the highlighted code
Create “SPI Commands Microphone ADC” subVI

## Slide 9
DETAILED INSTRUCTIONS:
Disconnect all Terminals
Right Click on the Icon in the right corner, select “Disconnect all terminals”
b) Create Front Panel Interface
Connect Front Panel Controls as shown in picture
SPI References to top left
SPI PHY Settings to left side, second from Top
Chip Select to Middle Top
Data To Device bottom left
Data From Device right side
c) Repaint subVI Icon
Repaint subVI Icon as shown in picture and give a name
“SPI CMDS MIC” as shown in the picture
Reconnect all the Front Panel Components
SPI API References
Chip Select
Data To
Device
SPI PHY Settings
Data From
Device

## Slide 10
DETAILED INSTRUCTIONS:
Add SPI Components to Ex-2 FPGA Block Diagram
Copy the following components from Ex-1 FPGA to Ex-2 FPGA
“SPI Engine Microphone ADC.vi”
“SPI Commands Microphone ADC.vi”
“Initialize SPI Internal References.vi”
Connect “SPI API Internal References”
  Wire the SPI API Internal Reference of Initialize SPI Internal References.vi input to the same named input of SPI Engine Microphone ADC.vi and SPI Commands Microphone ADC.vi
  Connect SPI PHY Settings to SPI CDMS SubVI.
Add SPI Components to Ex-2 FPGA
SPI Commands Microphone ADC.vi
SPI Engine Microphone ADC.vi
Initialize SPI Internal References.vi
SPI API Internal References

## Slide 11
DETAILED INSTRUCTIONS:
Create Constant for I/O Terminal
Right Click on the “Enable Lines” Terminal of SPI Engine and create a constant. Select the appropriate I/O terminals to match the ones in Ex-1
Create Constant for I/O Terminal Enable
Right Click on the “SPI DIO Lines” Terminal of SPI Engine and create constant. Select the appropriate I/O terminals to match the ones in Ex-1
Select the correct terminals to match Ex-1 I/O lines
Select the I/O terminals and enable terminals to match Ex-1. This is crucial step, it is very common to do simulation at this step to verify correctness of the code.
Create a Control for SPI PHY Settings
Right click on the “SPY PHY Settings” Terminal of the SPI Commands Microphone ADC.vi and create a control.
Check Completed FPGA Code
Check to ensure that final FPGA Code matches the picture shown in left
Completed Picture of FPGA Code
I/O constant for SCLK, CS, MOSI,MISO
I/O constant for SCLK, CS, MOSI,MISO Enable Lines

## Slide 12
DETAILED INSTRUCTIONS:
Save the EX-2 FPGA.vi
Press <Ctrl+S> or go to File » Save.
Compile the EX-2 FPGA.vi
Navigate to the Build Specifications category under the FPGA hierarchy. Expand this category and right-click on the existing FPGA VI and select Build as shown in Figure A
Fug
Compile the FPGA Code
Figure B
Figure A

## Slide 13
DETAILED INSTRUCTIONS:
LabVIEW prompts you to select the compile server. Select the local compile server and click OK as shown in Figure C. This will start the compilation process.
During the compilation process, LabVIEW generates intermediate HDL files that are later processed by the Xilinx Compiler, which outputs a bitfile containing the placing and routing information of the FPGA design.
The compilation process for this VI takes about 15 minutes. Once you have reached the Compilation Status window, as shown in Figure C, PROCEED TO next part to start developing the real-time portion of the application.
Compile the FPGA Code
Figure C
Figure D

## Slide 14
DETAILED INSTRUCTIONS:
Open the Ex-2 RT.vi
  Double-click on the file named Ex-2 RT.vi is located under the Real-Time target in the hierarchy as shown in Figure A
Open the Block Diagram
Look at the comments on the block diagram to understand the contents of the program. The flow of program should be similar to DAQmx.
We will modify this Ex-2 RT. vi to acquire input from a microphone after modifying the FPGA code.
Open the Ex-2 RT.vi and look at its block diagram
The Ex-2 RT.vi is located under the RT Target in the hierarchy. This file contains the user interface and the block diagram.
Waveform Acquisition Code on RT using cRIO Waveform Library

## Slide 15
DETAILED INSTRUCTIONS:
Add FPGA Property Node
  Place Read/Wrote Property Node on the block diagram by opening the Functions Palette and navigate to FPGA Interface >> Read/Write Property Node.
Insert FPGA Property Node
  Wire the output reference from the Run Method to the input reference of FPGA property node and then wire property method reference output to create channel.vi. Similarly, wire the error clusters to both sides of FPGA property node.
Modify the Ex-2 FPGA Code to add SPI Code
Add SPI Configuration Property Node before Create Channel.vi

## Slide 16
DETAILED INSTRUCTIONS:
Modify Property Node
Right click on the property node and select “SPI PHY Settings”
Create Control for SPI PHY Settings
Right click on the “SPI PHY Settings” and create control
Modify the Ex-2 RT Code to add SPI Attributes

## Slide 17
DETAILED INSTRUCTIONS:
Modify Property Node
Right click on the property node and select “SPI PHY Settings”
Create Control for SPI PHY Settings
Right click on the “SPI PHY Settings” and create control
Completed Picture of RT Code
SPI Settings can be adjusted
to meet microphone requirements

## Slide 18
DETAILED INSTRUCTIONS:
Modify SPI PHY Settings
Modify the “SPI PHY Settings” on the front panel to match the settings in Ex-1.
Run the Real-Time Code
After the FPGA Code is compiled, run “Ex-2 RT” Code
to acquire waveforms
Run the RT code
Modify these settings
to match with the
Microphone requirements

## Slide 19
DETAILED INSTRUCTIONS:
Collect waveforms
If you are able to collect waveforms as shown in Figure A, you are done with Exercise-2
Congratulations on finishing Exercise-2 !
End of Exercise-2